TTN_GPS_Tracker_Setup_Instructions

These instructions describe the building of a GPS tracker that uses The Things Network (TTN) to receive the trackers location. Once the location data is received by the TTN the trackers location can be viewed online on a Internet enabled device or passed to online mapping applications.

The build and testing of the tracker itself is described first. Then the configuration required for TTN is described and finally sending the trackers location from TTN into an online application, Cayenne in this case, is described.

The tracker node is a simple Arduino device with a GPS attached. An Arduino Pro Mini 3.3V is all that is required. The tracker software parses the location information from the GPS and sends the location as latitude and longitude using the LoRa device into the TTN network. There must therefore be a TTN gateway within reach of the tracker node. When correctly setup you should see the GPS location messages arriving in the TTN console. You will need a Things network account to view this console. You will also need to setup the TTN console to pass your tracker node information across to Cayenne and set up the Cayenne desktop to receive and display the information.

The TTN tracker node program code published here is for the Arduino environment and has been tested and runs on the Atmega328P. Note that the GPS and LoRa device are 3.3V logic devices, this is the reason a 3.3V Arduino Pro mini is the recommended device.

# Building the TTN_GPS_Tracker

Before loading and running the specific TTN_GPS_Tracker code on our node it is essential to test out the seperate component parts of the tracker, specifically the GPS and the LoRa device. If you do not assure yourself that these components are working before trying to run the TTN_GPS_Tracker code, if you then have problems you will have difficulty working out what the problems are.

## Testing the GPS
A very common problem reported with GPS trackers is that ‘the GPS does not work’. The TTN_GPS_Tracker code will not work without a functioning GPS so it is essential to test it first.
Load the EchoGPS_Softwareserial_Test.ino program into the Arduino IDE, makes sure the Arduino IDE is set to use the Arduino Pro Mini at 3.3V 8Mhz, see below;

Picture 1

The EchoGPS_Softwareserial_Test uses the softwareserial library program to read the GPS, you need to define the pins that the GPS is connected to, see these two defines at the start of the program;
#define GPSTX A2 //pin number for TX output - Arduino into GPS
#define GPSRX A3 //pin number for RX input - To Arduino from GPS
Also define the pin number that the LED is connected to, it will be used by the TTN_GPS_Tracker code. Some of the LoRaTracker boards allow the GPS to be powered off (such as the LCD receiver) if your board has this facility you need to define the pin used to control the GPS power, putting this pin low turns on the GPS;
#define GPSPOWER 7 //not used pin for non LoRaTracker boards
If your board does not have this capability define the pin as -1
Load the program and when it runs the LED should flash briefly at startup and then the serial monitor should show GPS output similar to this;

EchoGPS_Softwareserial_Test
10/10/2018
Stuart Robinson

b²±,,,,,,121018,,,N*6E
$GNVTG,,,,,,,,,N*2E
$GNGGA,102207.00,$GNRMC,102208.00,V,,,,,,,121018,,,N*61
$GNVTG,,,,,,,,,N*2E
$GNGGA,102208.00,,,,,0,00,99.99,,,,,,*71
$GNGSA,A,1,,,,,,,,,,,,,99.99,99.99,99.99*2E
$GNGSA,A,1,,,,,,,,,,,,,99.99,99.99,99.99*2E
$GPGSV,1,1,02,08,,,25,22,,,34*73
$GLGSV,1,1,00*65
$GNGLL,,,,,102208.00,V,N*5D
$GNRMC,102209.00,V,,,,,,,121018,,,N*60
$GNVTG,,,,,,,,,N*2E
$GNGGA,102209.00,,,,,0,00,99.99,,,,,,*70
$GNGSA,A,1,,,,,,,,,,,,,99.99,99.99,99.99*2E
$GNGSA,A,1,,,,,,,,,,,,,99.99,99.99,99.99*2E
$GPGSV,1,1,02,08,,,25,22,,,35*72
$GLGSV,1,1,00*65
$GNGLL,,,,,102209.00,V,N*5C
$GNRMC,102210.00,V,,,,,,,121018,,,N*68
$GNVTG,,,,,,,,,N*2E
$GNGGA,102210.00,,,,,0,00,99.99,,,,,,*78
$GNGSA,A,1,,,,,,,,,,,,,99.99,99.99,99.99*2E
$GNGSA,A,1,,,,,,,,,,,,,99.99,99.99,99.99*2E
$GPGSV,1,1,02,08,,,25,22,,,35*72
$GLGSV,1,1,00*65
$GNGLL,,,,,102210.00,V,N*54

Note that the two NMEA sentences that normally contain the location data, $GNGGA and $GNRMC are empty of the latitude and longitude data. This is normal for a GPS that has just been powered up or that is located indoors.
Whilst the above shows the GPS is working it has yet to get a location fix. It is important to check that the GPS does get a fix and that the GPS reports the location data. So take the GPS outdoors and monitor the serial monitor. Within a couple of minutes the GPS output should look like this;

GPS with fix output.

Note that a lot of the Ublox GPSs default to the $GNGGA and $GNRMC NMEA sentence format, other GPSs may use $GPGGA and $GPRMC formats. The GPS library used in the
TTN_GPS_Tracker code recognises both types.

## Testing the LoRa device

It is important to test that the LoRa device is connected correctly working before running the TTN_GPS_Tracker code.
Load the LoRa_Module_Test_868Mhz.ino program into the Arduino IDE, do not program the board yet. Your board needs to have the following pins defined in the program and connected to the LoRa device;

#define lora_NSS 10 //Arduino pin number for NSS on LoRa device
#define lora_NReset 9 //Arduino pin number for RESET pin on LoRa device
#define LED1 8 //Arduino pin number for LED, when high LED is on.

You also need to connect these pins;
Arduino LoRa Device
VCC 3.3V
GND GND
SCK (13) SCK
MISO (12) MISO
MOSI (11) MOSI

Pro Mini pin numbers shown in brackets. Connections to thew LoRa devices DIO0, DIO1 and DIO2 pins are not required for this test.
Program your board with the LoRa_Module_Test_868Mhz.ino program and when it runs the Arduino serial monitor output should show the following;

LoRa_Module_Test_868Mhz
V1.1
10/10/2018
Stuart Robinson

LED Flash

Checking LoRa Device

Registers after reset - LoRa Registers
Reg 0 1 2 3 4 5 6 7 8 9 A B C D E F
0x00 00 0F 1A 0B 00 52 6C 80 00 4F 09 2B 20 08 02 0A
0x10 FF 6F 15 0B 28 0C 12 47 32 3E 00 00 00 00 00 40
0x20 00 00 00 00 05 00 03 93 55 55 55 55 55 55 55 55
0x30 90 40 40 00 00 0F 00 00 00 F5 20 82 FD 02 80 40
0x40 00 00 12 24 2D 00 03 00 04 23 00 09 05 84 32 2B
0x50 14 00 00 11 00 00 00 0F E0 00 0C FD 07 00 5C 78
0x60 00 19 0C 4B CC 0E 7F 20 04 47 AF 3F B2 00 37 0B
0x70 D0 01 10 00 00 00 00 00 00 00 00 00 00 00 00 00
Frequency after reset - 434.000Mhz

Device Present

Registers after setup - LoRa Registers
Reg 0 1 2 3 4 5 6 7 8 9 A B C D E F
0x00 00 0F 1A 0B 00 52 6C 80 00 4F 09 2B 23 08 02 0A
0x10 FF 00 15 0B 28 0C 12 47 32 3E 00 00 00 00 00 FF
0x20 00 0C 00 00 05 00 03 93 55 55 55 55 55 55 55 55
0x30 90 40 40 00 00 0F 00 00 00 F5 20 82 FD 02 00 40
0x40 00 00 12 24 2D 00 03 00 04 23 00 09 05 84 32 2B
0x50 14 00 00 11 00 00 00 0F E0 00 0C 00 07 00 5C 78
0x60 00 19 0C 4B CC 0E 41 20 04 47 AF 3F B4 00 38 0B
0x70 D0 01 10 00 00 00 00 00 00 00 00 00 00 00 00 00
New Frequency - 868.000Mhz
Transmit FM Tone - Done

Note that at reset the LoRa device frequency is 434.000Mhz and the program changes the frequency to 868.000Mhz (New Frequency) and transmits an FM tone. Youy could use an SDR to listen for the tone.

# Setting up the TTN Console

With GPS and LoRa device working on our board we can move on to setting up the TTN console to accept the packets the TTN_GPS_Tracker will be transmitting.

The following instructions are based in part on this video, which is a simple to follow set of instructions for setting up a TTN node, I recommend you watch it;

https://www.youtube.com/watch?v=duwUwXt-hs8

## Create a Things Network Account (if you do not already have one)

Goto the Things Network website;

 https://www.thethingsnetwork.org/

And select the ‘Sign Up’ button at the top of the screen;

Picture 2

Provide the details for your new account, you will need an email address;

Picture 3

You will get an email with a link to confirm your account.

## Log into your Things Network Account

Goto the Things Network Website

https://www.thethingsnetwork.org/

And select the login button;

Picture 4

Once you have logged in drop down the menu against your name and select Console;

Picture 4A

## Configuring applications in the TTN console

Select applications;

Picture 4B

If you have created an application before you will see a list of them, otherwise you just see a screen like below, select ‘Add Application’ on the top right of the window below;

Give your application a name, but note these limitations; application ID can only consist of lowercase alphanumeric characters, with no consecutive – or _ characters and it cannot start or end with a - or a _ .

We call our application; ‘TTN_GPS_Tracker’

Picture 5

Ensure that the ttn-handler-eu is selected in the ‘Handler registration’ box.

When you have completed the form, click on ‘Add application’, and you will see the application overview.

There are no devices configured for the application, so we need to add one, click on devices at the top of the screen;

Then click on ‘register device’. Provide a name for the Device, such as ‘ttn_gps_tracker_1’ and enter it in the Device ID box. Enter a fake Device EUI such as 00 11 22 33 44 55 66 77, we can change it later. Then click on ‘Register’ bottom right of the screen;

We should then see the device overview screen;

Click on settings from the selection at the top of the device overview screen;

When the settings screen appears find the Activation Method box and ensure ABP is selected and highlighted. Then click ‘Save’ at the bottom of the screen.

We are using ABP activation so we need to copy the ‘Network Session Key’ and ‘App Session Key‘ into our Arduino program. Then Key box initially looks like this;

Click on the eye button to see the actual key and the <> to see the app key in a format that we will need to copy into the Arduino TTN_Node_Test program. Click on the button to the right of the Key, it will copy the Respective key into the clipboard so that we can then paste it into the program.

Open the TTN_GPS_Tracker.ino program in the Arduino IDE and find these lines in the configuration.h file, section ‘2) Program Options’;

NWKSKEY[16] = {0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00};

APPSKEY[16] = {0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00,0x00};

DEVADDR = 0x00000000;

Paste the Network Session Key from the TTN console into the NWKSKEY definition and the App Session Key into to the APPSKEY definition within the configuration file.

The console will also have generated a device address so copy Device address into the DEVADDR definition into the configuration file.

The completed entries should look like this, note the 0x added in front of the number and the removed spaces;

(for security reasons the actual key shown is not valid)

Be careful when copying not to create double sets of curly braces in the configuration file such as;

u1_t NWKSKEY[16] = { { 0x27, 0x55, 0xF2,
2) Program Options
## Loading the TTN_GPS_Tracker program
With the NWKSKEY, APPSKEY and DEVADDR entered into the configuration.h file load the program onto your board.

To see if the data your node is sending is going through the Things Network, login to your TTN account and goto the console. Select applications and then (for this example) select the loratracker_test_application byt clicking on the coloured button;

You should see this screen;

Click on ‘Data’ on the top right of the window and you should see the Application data packets arriving;

The payload is displayed in hexadecimal. 0X4C is ASCII ‘L’ and 0x6F is ASCII ‘o’ etc.

Note - Frame Counter

Each packet\payload that the node sends has a frame counter and the TTN network keeps track of them. If for example your node had sent 20 packets\payloads (frame counters 0-19) and you restart your node then the TTN network will ignore the packets until the frame counter reaches 20, then it will continue to display the payloads in the console again.

This behaviour can give the impression that your node is not working. You can disable this beahviour for testing purposes, by going to the Application overview screen, selecting ‘Devices’ then select the device to configure and then from the ‘Device Overview’

And then select ‘Settings’ on the top right.

At the bottom of the screen of device settings you will see this box, ‘frame counter settings’

You can untick this box, and when the node resets the frame counter will start from zero and the packets\payloads will not now be rejected. This is OK when testing a node, but do not leave it permanently set.

You have completed your node configuration. You can now carry out a test of the TTN_GPS_Tracker node.

## Create a Cayenne Account

Goto http://www.mydevices.com

## TTN_GPS_Tracker program – Display option

Note that the TTN_GPS_Tracker program has the option to display information on a local display, either a 20x4 LCD display or a SSD1306 OLED, this option is turned off by default because of this line in the configuration file;

//#define Use_Display

The two // characters turn the text that follows into a comment which is ignored by the Arduino compiler. To enable the display option we would change the line into;

#define Use_Display

Do not enable the display option unless a display is actually attached and working.

Stuart Robinson
June 2018